## Slide 1
NetZone
Network Segmentation & Access Control Design
Enterprise VLAN Segmentation · ACL Access Policies · Hierarchical Three-Tier Architecture
Arsanious Nashaat – 240101749
Hoda Hossam – 240100541
Jana Mostafa – 240103050
Khaled Ahmed – 240101436
Mahmoud Ehab – 240102397

## Slide 2
Project Overview
5 VLANs
Admin · Finance · HR · POS · Guest
3-Tier Hierarchy
Core / Distribution / Access
Extended ACLs
Named ACLs on MLS + Router
Key Objectives
Segment the network into five isolated VLANs by department
Enable inter-VLAN routing via a Layer 3 multilayer switch
Enforce granular access control between departments using ACLs
Block the Guest VLAN from all internal resources and the internet
Provide internet access to all departments except Guest

## Slide 3
Network Topology
CORE LAYER
Cisco 2901 Router0
Internet via gig0/1 · Downlink to MLS via gig0/0
DISTRIBUTION LAYER
Cisco 3560-24PS Multilayer Switch0
Inter-VLAN routing via SVIs · Uplinks gig1/0/1–5
ACCESS LAYER
4× Cisco 2960-24TT (Admin, Finance, HR, POS)
Each trunked to MLS via fa0/3
⚠ Guest VLAN (VLAN 50): Dedicated 2960-24TT connects directly to Router0 fa0/1, bypassing the multilayer switch entirely for security isolation.

## Slide 4
IP Addressing & VLAN Scheme
VLAN | Name | Subnet | Gateway | Devices
VLAN 10 | Admin | 192.168.2.0/24 | 192.168.2.1 | PC0, PC1
VLAN 20 | Finance | 192.168.3.0/24 | 192.168.3.1 | PC2, PC3
VLAN 30 | HR | 192.168.4.0/24 | 192.168.4.1 | PC4, Laptop0
VLAN 40 | POS | 192.168.5.0/24 | 192.168.5.1 | PC5, Server1
VLAN 50 | Guest | 192.168.6.0/24 | 192.168.6.1 | PC6, Laptop1
All VLANs route through SVIs on Multilayer Switch0 except Guest (routes via Router0 fa0/1)

## Slide 5
Access Control Policy
Admin (VLAN 10)
Full access — all VLANs + internet. No restrictions.
✔
Finance (VLAN 20)
Reaches Admin, POS, Internet. Blocked from HR & Guest.
⚠
HR (VLAN 30)
Reaches Admin, POS, Internet. Blocked from Finance & Guest.
⚠
POS (VLAN 40)
Reaches all internal VLANs + Internet. No outbound restrictions.
✔
Guest (VLAN 50)
BLOCKED from everything — all internal VLANs AND internet.
✘

## Slide 6
ACL Traffic Matrix
Source \ Dest
Admin (10)
Finance (20)
HR (30)
POS (40)
Guest (50)
Admin (10)
✔ Allow
✔ Allow
✔ Allow
✔ Allow
✔ Allow
Finance (20)
✔ Allow
—
✘ Deny
✔ Allow
✘ Deny
HR (30)
✔ Allow
✘ Deny
—
✔ Allow
✘ Deny
POS (40)
✔ Allow
✔ Allow
✔ Allow
✔ Allow
✘ Deny
Guest (50)
✘ Deny
✘ Deny
✘ Deny
✘ Deny
—
✔ Allow = Traffic permitted ✘ Deny = Traffic blocked by ACL — = Same VLAN

## Slide 7
ACL Configuration Highlights
ACL-FINANCE (MLS VLAN 20 SVI)
deny → HR (192.168.4.0)
deny → Guest (192.168.6.0)
permit → POS (192.168.5.0)
permit → any (internet)
ACL-HR (MLS VLAN 30 SVI)
deny → Finance (192.168.3.0)
deny → Guest (192.168.6.0)
permit → POS (192.168.5.0)
permit → any (internet)
ACL-GUEST (Router0 fa0/1)
deny icmp echo → Admin
deny icmp echo → Finance
deny icmp echo → HR
deny icmp echo → POS
permit ip any any (return traffic)
Placement Principle
ACLs applied inbound on SVI
Filters traffic before routing
Guest ACL on Router fa0/1 since
Guest switch bypasses the MLS

## Slide 8
Verification & Testing Results
Source | Destination | Result
Admin PC0 | Finance PC2 | SUCCESS
Admin PC0 | HR PC4 | SUCCESS
Admin PC0 | 8.8.8.8 (Internet) | SUCCESS
Finance PC2 | HR PC4 | DENIED – ACL-FINANCE
Finance PC2 | POS PC5 | SUCCESS
HR PC4 | Finance PC2 | DENIED – ACL-HR
HR PC4 | POS PC5 | SUCCESS
Guest PC6 | Admin PC0 | DENIED – ACL-GUEST
Guest PC6 | 8.8.8.8 (Internet) | DENIED – blocked
POS Server1 | Finance PC2 | SUCCESS

## Slide 9
Troubleshooting Guide
Ping fails between VLANs where it should succeed
Verify ip routing on MLS; check trunk links; confirm SVIs are up/up
ACL not filtering traffic
Verify ACL applied to correct interface/direction; check hit counters with show ip access-lists
Guest can still reach internal VLANs
Confirm ACL-GUEST is on Router0 fa0/1 (inbound), not on MLS
Finance can reach HR (should be blocked)
Confirm ACL-FINANCE lines are in correct order; ACLs process top-down
Internet fails for all VLANs
Check default route toward ISP; verify NAT/PAT configuration
Trunk ports not passing VLANs
Run show vlan brief to confirm VLANs exist; check allowed VLAN list on trunks

## Slide 10
Project Summary
Designed a hierarchical three-tier enterprise network in Cisco Packet Tracer
Configured 5 VLANs with dedicated /24 subnets and inter-VLAN routing via SVIs
Applied extended named ACLs on the Multilayer Switch and Router to enforce departmental isolation
Completely isolated the Guest VLAN from internal resources and the internet
Verified all policies through PDU simulation and ping test matrix with expected results
Documented full configuration, verification commands, and troubleshooting guide
NetZone · Network Segmentation & Access Control · Cisco Packet Tracer